## Slide 1: Carrying Binding Label/SID in PCE-based Networks.
draft-sivabalan-pce-binding-label-sid-05
Siva Sivabalan | Clarence Filsfils | Jeff Tantsura | Jonathan Hardwick | Stefano Previdi | Dhruv Dhody

## Slide 2: Introduction & Motivation
SR [RFC8402] defined Binding Segment (BSID)
  Bound to a SID list (SR policy)
BSID provides greater
  Scalability
  Network Opacity
  Service Independence
Decrease the number of segments imposed by the source.
Act as a stable anchor point and isolate one domain from another.
BSID remains stable and hide internal details.

## Slide 3: Role of PCEP
PCC could report the BSID allocated for the LSP
  PCRpt message
PCE could request the PCC to allocate specific BSID for the LSP
  PCUpd / PCInitiate message
PCE could use the BSID while computing SID list (SR-ERO) for some other SR Path as per [I-D. ietf-pce-segment-routing]
Path Binding TLV is defined for LSP object!

## Slide 4: Binding TLV
TE-PATH-BINDING TLV in the LSP object
BT=0 for MPLS Label value
  20 bit label value
BT=1 for MPLS Label stack entry (TC, S, TTL)
  32 bit label stack entry

## Slide 5: Question to WG & Next Steps
The feature is very useful and already implemented, ideal for WG Adoption?
Some things to work out –
  Do we link to PCEP SR capability?
    Currently can be used for RSVP-TE as well.
  Is WG happy with TLV Format?
  Is there a use case for binding value as “index” in SRGB/SRLB?
  Move the appendix section on PCECC to PCECC-SR draft
    PCECC could also assign the BSID to the LSP.

## Slide 6
Thanks!