## Slide 1: A Yang Data Model for ACTN VN Operation draft-ietf-teas-actn-vn-yang-02
Young Lee, Dhruv Dhody, Daniele Ceccarelli
Igor Bryskin, Bin Yeong Yoon, Qin Wu, Peter Park

## Slide 2: ACTN Yang Model Map
TE Topology
TE Tunnel
VN
L3SM
Augmented with underlying TE
L2SM
Augmented with underlying TE
L1CSM
Augmented with underlying TE
Service Models
TE Models

## Slide 3: ACTN VN Yang
Yang model for Virtual Network Service (VNS) operations
From the point of view of Customer
An abstraction over the TE-Topo and TE-Tunnel
These models are from the point of view of Network
Some similarity, but still different!
VN is a higher level of abstraction than topology!
VN depends on topology!

## Slide 4: Relationship
ACTN VN
Single node in TE Topology
Native TE Topology
abstract topology
In case of VN Type 2 operations, customer could access!
Customer
Network

## Slide 5
ACTN VN
AP
VNAP
VN
VN-Member
From
To
Node
connectivity-matrices
underlay
primary-path
path-constraints
Optimizations
computed-path-properties
connectivity-matrix [id]
From
underlay
Primary-path
path-constraints
Optimizations
To
tunnel-termination-points
tunnel
global
Per entry

## Slide 6: Overview
ACTN VN Yang Model
AP/VNAP
VN
VN-Member
Abstract Topology with a
Single Node
Underlay
For both VN Type 1 or Type 2 VN Yang model rely on a single node in the abstract TE Topology
The abstract node has
  connectivity-matrices
  connectivity-matrix [id]
  The attributes directly under container connectivity-matrices are the default attributes for all connectivity-matrix entries when the per entry corresponding attribute is not specified. When a per entry attribute is specified, it overrides the corresponding attribute directly under the container connectivity-matrices.
Connectivity
Matrix

## Slide 7: VN Type 1
VN 1
  VN-Member 1 L1-L4
  VN-Member 2 L1-L7
  VN-Member 3 L2-L4
  VN-Member 4 L3-L8
  This VN has following properties
    Bandwidth 500
    Optimize by delay
Abstract Topology with a
Single Node
14: L1-L4 | 17: L1-L7
24: L2-L4 | 38: L3-L8
Connectivity
Matrix
Attributes
  connectivity-matrices
  These properties
  are set in TE Topo
VN is seen as edge to edge links (VN-members) setup as tunnels across underlying networks!

## Slide 8: VN Type 2
VN is seems as a topology of virtual nodes and links
To ease mapping between VN Yang Model and TE models, an abstract single node topology is created with VN topology as the underlay!
The same mapping as VN Type 1 is reused.
VN 2
  VN-Member 1: L1-L8 via S3, S67110, S11
    Set via the underlay path in connectivity-matrix[id]
S3
S9
S124
S67110
S5
S8
S11
Abstract Topology with a
Single Node
VN Topology
Underlay
Underlay

## Slide 9: ACTN Info Model [RFC 8454]
VN Action primitives on CMI -
  VN Instantiate
  VN Modify
  VN Delete
  VN Update
  VN Path Compute
  VN Query
Maps to actions on ACTN VN Yang model easily
  But, with dependency on the TE topology model when it comes to details such as constraints, actual path etc

## Slide 10: ACTN VN Operations
VN could be explicitly created via this yang model
VN could also be auto-created based on the service model
  With a service mapping to the VN
  Via ACTN VN abstraction, customer could learn how the network fulfills the service!
Further allow some new interesting services!
  Multi-Source / Multi-Destination
  VN Compute

## Slide 11: Status
Adopted as WG draft after IETF 101.
Relationship between other models clarified
  Suggest further improvements
Security & IANA considerations updated

## Slide 12: BACKUP!

## Slide 13: How: Reference to TE Topology Yang Model
Access | AP/ VNAP -> LTP Ltp of type te-types:te-tp-id
Customer’s Virtual Network | VN -> Abstract Node vn-topology-id of type te-types:te-topology-id abstract-node -> /nw:networks/network/node/tet:te-node-id (reference)
Customer Site to Site connection | VN-Member -> Entry in the connectivity matrix of the abstract node connectivity-matrix-id -> /nw:networks/network/node/tet:te/te- node-attributes/connectivity-matrices/connectivity-matrix/id (reference)
All parameters which are can be set as global attributes to VN are set in the connectivity-matrices (such as bandwidth) and an attribute for a particular VN-member is set in the connectivity-matrix [id] (such as explicit path)!
Duplicate parameters in ACTN VN Yang model are removed!