## Slide 1: PCEP for SRv6
draft-negi-pce-segment-routing-ipv6-03
draft-dhody-pce-pcep-srv6-yang-00
Mahendra Singh Negi | Dhruv Dhody | Siva Sivabalan | Prejeeth Kaladharan
Huawei |  | Cisco | RtBrick

## Slide 2: Introduction & Motivation
Segment Routing (SR) can be used to steer packets through an IPv6 or MPLS network using the source routing paradigm.
Since SR can be applied to both MPLS and IPv6 data plane
  A PCE be able to compute SR-Path for both MPLS and IPv6 forwarding plane
    Segment identified by an IPv6 address
    SID list as a list of IPv6 address (encoded in the SRH)
PCEP Extension to support SRv6
  Extended SR-ERO, SR-RRO sub-objects for SRv6
  Capability advertisement for SRv6 in PCEP
  A new path setup type for SRv6

## Slide 3: SRH & SRv6 SID
128 Bit
Payload
128 Bit
128 Bit
128 Bit
IP Header
Locator
Function(ARG)
IPV6 SRH HEADER
The “Function” can identify the L2VPN/L3VPN, and other services or APP.
Version | Traffic Class | Flow Label |  | 
Pload Length |  |  | Next=43 | Hop Linmit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List[0] |  |  |  | 
Segment List[1] |  |  |  | 
Segment List[2] |  |  |  | 
Paylod |  |  |  | 

## Slide 4: Update
Update the SRv6 Capability handling
  As per the PST and PCEP-SR
  SRv6-PCE-CAPABILITY sub-TLV is defined
Alignment with PCEP-SR
  Use of NAI-Type (NT) instead of SID-Type (ST)
  Error Handling
  SR-ERO interpretation
  SRv6NT = Node ~ LOC
SRv6-PCE-CAPABILITY sub-TLV
SR-ERO Sub-object
SRv6I

## Slide 5: SRv6 Yang
Capability for SRv6
  Max-SL
A feature for SRv6
A new PST for SRv6
A SRv6 Path
  List of SRv6 SID (IPv6 address)

## Slide 6: Questions & Next Steps
Support for SRv6 in PCEP is a reasonable requirement!
Is this the right approach?
Is this a good base for the WG to consider adoption?
  draft-negi-pce-segment-routing-ipv6-03
Refine the document!

## Slide 7: Thank You!